NicE Buoy Manual
# Installation
To setup the buoy we have to do two things first.
1	Calibrating the compass
2	Calibrating the heading

# Calibrate comas
Press and hold the button when turning the Buoy power on.
Wait for 5 seconds. The buoy will beeb.
The red power light will flash.
Turn the buoy around in al direction and all axes for more than one minute. When the led is green and a beep has sounded the buoy compass calibration is done.

# Calibrate heading
Mark the place where the buoy is laying.
Turn the buoy on and wait until the green powered is on continues on.
Push the button for 5 seconds.. A beep will be generated an the button will flash.
Put the buoy more than 50 meters form the marked spot.
Point the buoy front to the marked place
Push the button again for more than 5 seconds.
The heading calibration is done.